## Slide 1: Interconnection Networks: Topology and Routing

## Slide 2: Topology Overview
Definition: determines arrangement of channels and nodes in network
Analogous to road map
Often first step in network design
Routing and flow control build on properties of topology

## Slide 3: Abstract Metrics
Use metrics to evaluate performance and cost of topology
Also influenced by routing/flow control
  At this stage
    Assume ideal routing (perfect load balancing)
    Assume ideal flow control (no idle cycles on any channel)
Switch Degree: number of links at a node
  Proxy for estimating cost
    Higher degree requires more links and port counts at each router

## Slide 4: Latency
Time for packet to traverse network
  Start: head arrives at input port
  End: tail departs output port
Latency = Head latency + serialization latency
  Serialization latency: time for packet with Length L to cross channel with bandwidth b (L/b)
Hop Count: the number of links traversed between source and destination
  Proxy for network latency
  Per hop latency with zero load

## Slide 5: Impact of Topology on Latency
Impacts average minimum hop count
Impact average distance between routers
Bandwidth

## Slide 6: Throughput
Data rate (bits/sec) that the network accepts per input port
Max throughput occurs when one channel saturates
  Network cannot accept any more traffic
Channel Load
  Amount of traffic through channel c if each input node injects 1 packet in the network

## Slide 7: Maximum channel load
Channel with largest fraction of traffic
Max throughput for network occurs when channel saturates
  Bottleneck channel

## Slide 8: Bisection Bandwidth
Cuts partition all the nodes into two disjoint sets
  Bandwidth of a cut
Bisection
  A cut which divides all nodes into nearly half
  Channel bisection  min. channel count over all bisections
  Bisection bandwidth min. bandwidth over all bisections
With uniform traffic
  ½ of traffic cross bisection

## Slide 9: Throughput Example
Bisection = 4 (2 in each direction)
0
1
2
3
4
5
6
7
With uniform random traffic
  3 sends 1/8 of its traffic to 4,5,6
  3 sends 1/16 of its traffic to 7 (2 possible shortest paths)
  2 sends 1/8 of its traffic to 4,5
  Etc
Channel load = 1

## Slide 10: Path Diversity
Multiple minimum length paths between source and destination pair
Fault tolerance
Better load balancing in network
Routing algorithm should be able to exploit path diversity
We’ll see shortly
  Butterfly has no path diversity
  Torus can exploit path diversity

## Slide 11: Path Diversity (2)
Edge disjoint paths: no links in common
Node disjoint paths: no nodes in common except source and destination
If j = minimum number of edge/node disjoint paths between any source-destination pair
  Network can tolerate j link/node failures

## Slide 12: Symmetry
Vertex symmetric:
  An automorphism exists that maps any node a onto another node b
  Topology same from point of view of all nodes
Edge symmetric:
  An automorphism exists that maps any channel a onto another channel b

## Slide 13: Direct & Indirect Networks
Direct: Every switch also network end point
  Ex: Torus
Indirect: Not all switches are end points
  Ex: Butterfly

## Slide 14: Torus (1)
K-ary n-cube: kn network nodes
n-dimensional grid with k nodes in each dimension
3-ary 2-cube
3-ary 2-mesh
2,3,4-ary 3-mesh

## Slide 15: Torus (2)
Topologies in Torus Family
  Ring k-ary 1-cube
  Hypercubes 2-ary n-cube
Edge Symmetric
  Good for load balancing
  Removing wrap-around links for mesh loses edge symmetry
    More traffic concentrated on center channels
Good path diversity
Exploit locality for near-neighbor traffic

## Slide 16: Implementation
Folding
  Equalize path lengths
    Reduces max link length
    Increases length of other links
0
1
2
3
0
1
2
3

## Slide 17: Concentration
Don’t need 1:1 ratio of network nodes and cores/memory
Ex: 4 cores concentrated to 1 router

## Slide 18: Butterfly
K-ary n-fly: kn network nodes
Example: 2-ary 3-fly
Routing from 000 to 010
  Dest address used to directly route packet
  Bit n used to select output port at stage n
0
00
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
01
02
03
10
11
12
13
20
21
22
23
0
1
0

## Slide 19: Flattened Butterfly
Proposed by Kim et al (ISCA 2007)
  Adapted for on-chip (MICRO 2007)
Advantages
  Max distance between nodes = 2 hops
  Lower latency and improved throughput compared to mesh
Disadvantages
  Requires higher port count on switches (than mesh, torus)
  Long global wires
  Need non-minimal routing to balance load

## Slide 20: Flattened Butterfly
Path diversity through non-minimal routes

## Slide 21: Clos Network
nxm input switch
nxm input switch
nxm input switch
nxm input switch
rxr input switch
rxr input switch
rxr input switch
rxr input switch
rxr input switch
mxn output switch
mxn output switch
mxn output switch
mxn output switch

## Slide 22: Clos Network
3-stage indirect network
Characterized by triple (m, n, r)
  M: # of middle stage switches
  N: # of input/output ports on input/output switches
  R: # of input/output switching
Hop Count = 4

## Slide 23: Folded Clos (Fat Tree)
Bandwidth remains constant at each level
Regular Tree: Bandwidth decreases closer to root

## Slide 24: Fat Tree (2)
Provides path diversity

## Slide 25: Common On-Chip Topologies
Torus family: mesh, concentrated mesh, ring
  Extending to 3D stacked architectures
  Favored for low port count switches
Butterfly family: Flattened butterfly

## Slide 26: Topology Summary
First network design decision
Critical impact on network latency and throughput
  Hop count provides first order approximation of message latency
  Bottleneck channels determine saturation throughput

## Slide 27: Routing Overview
Discussion of topologies assumed ideal routing
Practically though routing algorithms are not ideal
Discuss various classes of routing algorithms
  Deterministic, Oblivious, Adaptive
Various implementation issues
  Deadlock

## Slide 28: Routing Basics
Once topology is fixed
Routing algorithm determines path(s) from source to destination

## Slide 29: Routing Algorithm Attributes
Number of destinations
  Unicast, Multicast, Broadcast?
Adaptivity
  Oblivious or Adaptive? Local or Global knowledge?
Implementation
  Source or node routing?
  Table or circuit?

## Slide 30: Oblivious
Routing decisions are made without regard to network state
  Keeps algorithms simple
  Unable to adapt
Deterministic algorithms are a subset of oblivious

## Slide 31: Deterministic
All messages from Src to Dest will traverse the same path
Common example: Dimension Order Routing (DOR)
  Message traverses network dimension by dimension
  Aka XY routing
Cons:
  Eliminates any path diversity provided by topology
  Poor load balancing
Pros:
  Simple and inexpensive to implement
  Deadlock free

## Slide 32: Valiant’s Routing Algorithm
To route from s to d, randomly choose intermediate node d’
  Route from s to d’ and from d’ to d.
Randomizes any traffic pattern
  All patterns appear to be uniform random
  Balances network load
Non-minimal
d’
d
s

## Slide 33: Minimal Oblivious
Valiant’s: Load balancing comes at expense of significant hop count increase
  Destroys locality
Minimal Oblivious: achieve some load balancing, but use shortest paths
  d’ must lie within minimum quadrant
  6 options for d’
  Only 3 different paths
d
s

## Slide 34: Adaptive
Uses network state to make routing decisions
  Buffer occupancies often used
  Couple with flow control mechanism
Local information readily available
  Global information more costly to obtain
  Network state can change rapidly
  Use of local information can lead to non-optimal choices
Can be minimal or non-minimal

## Slide 35: Minimal Adaptive Routing
Local info can result in sub-optimal choices
d
s

## Slide 36: Non-minimal adaptive
Fully adaptive
Not restricted to take shortest path
  Example: FBfly
Misrouting: directing packet along non-productive channel
  Priority given to productive output
  Some algorithms forbid U-turns
Livelock potential: traversing network without ever reaching destination
  Mechanism to guarantee forward progress
    Limit number of misroutings

## Slide 37: Non-minimal routing example
Longer path with potentially lower latency
d
s
d
s
Livelock: continue routing in cycle

## Slide 38: Routing Deadlock
Without routing restrictions, a resource cycle can occur
  Leads to deadlock
A
B
D
C

## Slide 39: Turn Model Routing
Some adaptivity by removing 2 of 8 turns
  Remains deadlock free (like DOR)
West first
North last
Negative first

## Slide 40: Turn Model Routing Deadlock
Not a valid turn elimination
  Resource cycle results

## Slide 41: Routing Implementation
Source tables
  Entire route specified at source
  Avoids per-hop routing latency
  Unable to adapt to network conditions
  Can specify multiple routes per destination
Node tables
  Store only next routes at each node
  Smaller tables than source routing
  Adds per-hop routing latency
  Can adapt to network conditions
    Specify multiple possible outputs per destination

## Slide 42: Implementation
Combinational circuits can be used
  Simple (e.g. DOR): low router overhead
  Specific to one topology and one routing algorithm
    Limits fault tolerance
Tables can be updated to reflect new configuration, network faults, etc

## Slide 43: Circuit Based
sx
x
sy
y
=0
=0
Route selection
Productive Direction Vector
+x
-x
+y
-y
exit
Queue lengths
Selected Direction Vector
+x
-x
+y
-y
exit

## Slide 44: Routing Summary
Latency paramount concern
  Minimal routing most common for NoC
  Non-minimal can avoid congestion and deliver low latency
To date: research favors DOR for simplicity and deadlock freedom
  On-chip networks often lightly loaded
Only covered unicast routing
  Recent work on extending on-chip routing to support multicast

## Slide 46: Multicast
Why multicast ?
Classification
  Path-based
  Tree-based

## Slide 47: Unicast
Src

## Slide 48: Unicast
Src

## Slide 49: Unicast
Src

## Slide 50: Unicast
Src

## Slide 51: Unicast
Src

## Slide 52: Unicast
Src

## Slide 53: Multicast
Src

## Slide 54: Multicast
Src

## Slide 55: Multicast
Src

## Slide 56: Multicast
Src

## Slide 57: Multicast
Src

## Slide 58: Multicast
Src

## Slide 59: Multicast
Path based
  Hamiltonian path

## Slide 60: Multicast
Tree based
  Replicate
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Source
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Destination

## Slide 61: Bibliography
Topology
  William J. Dally and C. L Seitz. The torus routing chip. Journal of Distributed Computing, 1(3):187–196, 1986.
  Charles Leiserson. Fat-trees: Universal networks for hardware efficient supercomputing. IEEE Transactions on Computers, 34(10), October 1985.
  Boris Grot, Joel Hestness, Stephen W. Keckler, and OnurMutlu. Express cube topologies for on-chip networks. In Proceedings of the International Symposium on High Performance Computer Architecture, February 2009.
  Flattened butterﬂy topology for on-chip networks. In Proceedings of the 40th International Symposium on Microarchitecture, December 2007.
  J. Balfour and W. Dally. Design tradeoﬀs for tiled cmp on-chip networks. In Proceedings of the International Conference on Supercomputing, 2006.
Routing
  L. G. Valiant and G. J. Brebner. Universal schemes for parallel communication. In Proceedings of the 13th Annual ACM Symposium on Theory of Computing, pages 263–277, 1981.
  D. Seo, A. Ali, W.-T. Lim, N. Raﬁque, and M. Thottenhodi. Near-optimal worst- case throughput routing in two dimensional mesh networks. In Proceedings of the 32nd Annual International Symposium on Computer Architecture, June.
  Christopher J. Glass and Lionel M. Ni. The turn model for adaptive routing. In Proceedings of the International Symposium on Computer Architecture, 1992.
  P. Gratz, B. Grot, and S. W. Keckler, “Regional congestion awareness for load balance in networks-on-chip,” in Proceedings of the 14th IEEE International Symposium on High-Performance Computer Architecture, February 2008.
  N. EnrightJerger, L.-S. Peh, and M. H. Lipasti, “Virtual circuit tree multi- casting: A case for on-chip hardware multicast support,” in Proceedings of the International Symposium on Computer Architecture (ISCA-35), Beijing, China, June 2008.